## Slide 1: REVIEW 2
Helly Dhamesha
Rahul Gandhi
20BRS1171
20BRS1264

## Slide 2: Predictive maintenance
MODULE 1: Conveyor Belts
MODULE 2: Milling machine
MODULE 3: Hydraulics

## Slide 3: MODULE 1: Conveyor belt
Dataset: Synthetically generated based on industry given values.
Algorithm: Classification method used to classify as in need of maintenance of not.
Accuracy results:
Precision : 0.9922
Recall or Sensitivity : 0.9101
Classification error : 0.0903

## Slide 4: MODULE 2: Milling machine
Dataset: Synthetically generated sourced from Kaggle, based on a research paper (from 2021) published about milling activities.
Competitive algorithm testing:
Logistical Classification
Decision Tree, Random Forest and Gradient Boosting Classifier
Neural Network MLP
Comparative Accuracy results: Overall ranks Random Forest
Notes: d after an existing milling machine and consists of 10 000 data points from a stored as rows with 14 features in columns
UID: unique identifier ranging from 1 to 10000
product ID: consisting of a letter L, M, or H for low (50% of all products), medium (30%) and high (20%) as product quality variants and a variant-specific serial number
type: just the product type L, M or H from column 2
air temperature [K]: generated using a random walk process later normalized to a standard deviation of 2 K around 300 K
process temperature [K]: generated using a random walk process normalized to a standard deviation of 1 K, added to the air temperature plus 10 K.
rotational speed [rpm]: calculated from a power of 2860 W, overlaid with a normally distributed noise
torque [Nm]: torque values are normally distributed around 40 Nm with a SD = 10 Nm and no negative values.
tool wear [min]: The quality variants H/M/L add 5/3/2 minutes of tool wear to the used tool in the process.
a 'machine failure' label that indicates, whether the machine has failed in this particular datapoint for any of the following failure modes are true.
The machine failure consists of five independent failure modes
tool wear failure (TWF): the tool will be replaced of fail at a randomly selected tool wear time between 200 - 240 mins (120 times in our dataset). At this point in time, the tool is replaced 69 times, and fails 51 times (randomly assigned).
heat dissipation failure (HDF): heat dissipation causes a process failure, if the difference between air- and process temperature is below 8.6 K and the tools rotational speed is below 1380 rpm. This is the case for 115 data points.
power failure (PWF): the product of torque and rotational speed (in rad/s) equals the power required for the process. If this power is below 3500 W or above 9000 W, the process fails, which is the case 95 times in our dataset.
overstrain failure (OSF): if the product of tool wear and torque exceeds 11,000 minNm for the L product variant (12,000 M, 13,000 H), the process fails due to overstrain. This is true for 98 datapoints.
random failures (RNF): each process has a chance of 0,1 % to fail regardless of its process parameters. This is the case for only 5 datapoints, less than could be expected for 10,000 datapoints in our dataset.
If at least one of the above failure modes is true, the process fails and the 'machine failure' label is set to 1. It is therefore not transparent to the machine learning method, which of the failure modes has caused the process to fail. This dataset is part of the following publication, please cite when using this dataset: S. Matzka, "Explainable Artificial Intelligence for Predictive Maintenance Applications," 2020 Third International Conference on Artificial Intelligence for Industries (AI4I), 2020, pp. 69-74, doi: 10.1109/AI4I49448.2020.00023.

## Slide 5: MODULE 3: Hydraulics
Dataset: Real open source dataset regarding real time data from Automobile manufacture
Attributes: Cooler condition, valve condition, internal pump leakage, hydraulic accumulator, stable flag.
Algorithm and accuracy:
TPOTClassifier – 98.18
Logistic Regression – 98.86
K neighbors classifier – 98.62
Notes: The data set contains raw process sensor data (i.e. without feature extraction) which are structured as matrices (tab-delimited) with the rows representing the cycles and the columns the data points within a cycle. The target condition values are cycle-wise annotated in ‘profile.txt‘ (tab-delimited). As before, the row number represents the cycle number. The columns are
1: Cooler condition / %:
3: close to total failure 20: reduced efficiency 100: full efficiency
2: Valve condition / %:
100: optimal switching behavior 90: small lag 80: severe lag 73: close to total failure
3: Internal pump leakage:
0: no leakage 1: weak leakage 2: severe leakage
4: Hydraulic accumulator / bar:
130: optimal pressure 115: slightly reduced pressure 100: severely reduced pressure 90: close to total failure
5: stable flag:
0: conditions were stable 1: static conditions might not have been reached yet

## Slide 6: ADDITIONAL FEATURES
TELEGRAM ALERT
Sends an alert message to the set manager on telegram
ADD TO GOOGLE CALENDAR
Automatically adds a slot for maintenance in the google account of the maintenance personal
SEND AN EMAIL
Automatically generates and sends emails to both the manager and the maintenance personal

## Slide 7: THANK YOU
Conveyor Belts: https://colab.research.google.com/drive/1vh7zjRfJX3L3uxvQHBT-AB1Ohmh-e6ts?usp=sharing
Milling System: https://colab.research.google.com/drive/16CzH6cfe61sn0Xrfl7A1H5s_vw_tqBSF?usp=sharing
Hydraulic systems: https://colab.research.google.com/drive/1zj3dypfNVQl2qERcXGDwKuwnmaHT-r6h?usp=sharing